## Slide 1
April 10, 2026
F-150 Purchase Analysis
Presentation to the Board of the Village of Tuxedo Park

## Slide 2
What was modeled
Four acquisition paths, tested over three ownership periods and three annual-mileage cases
Vehicle options
Scenario
Vehicle basis
New F-150 gas
2025 F-150 XLT, internal-combustion
New F-150 Lightning
2025 F-150 Lightning XLT
Used F-150 gas
2023 F-150 XLT used-market anchor
Used F-150 Lightning
2023 F-150 Lightning XLT used-market anchor
Ownership periods tested
3 years
5 years
7 years
Mileage scenarios
12k / yr
15k / yr
20k / yr
Included in total cost of ownership
Purchase price less expected resale value at the end of the holding period
Fuel or electricity based on NY prices and the municipal-facility charging assumption
Insurance and maintenance using pickup-truck benchmarks
The $500 NYSERDA Drive Clean Rebate on a new Lightning only
Excluded from the vehicle TCO table
Financing, sales tax, and registration
Charger purchase and make-ready costs
Site incentives that depend on final project design
Notes: [Sources] - Ford 2025 F-150 pricing/specs: https://www.ford.com/trucks/f150/2025/ - Ford 2025 F-150 Lightning pricing/specs: https://www.ford.com/trucks/f150-lightning/ - NYSERDA Drive Clean Rebate: https://www.nyserda.ny.gov/All-Programs/Drive-Clean-Rebate-For-Electric-Cars-Program - O&R POWERREADY: https://www.oru.com/en/our-energy-future/electric-vehicles/new-york/commercial-ev-drivers/power-ready-program

## Slide 3
Executive summary
Result is robust across all tested mileage and ownership-period cases
Recommendation
Buy the used
F-150 Lightning
Lowest modeled total cost in all 9 mileage / horizon combinations tested
Best 5-year TCO at 15k miles/year: $41.8k vs. $49.3k for a new gas F-150
Advantage comes from both a lower used purchase price and lower annual energy / maintenance costs
Operational caveat: heavy towing or frequent long-distance towing still favors the gas truck
5-year cost at 15,000 miles/year
Chart: 
| Used F-150 Lightning | New F-150 gas | Used F-150 gas | New F-150 Lightning
5-year TCO | 41.8 | 49.3 | 50.7 | 63
Why the used Lightning wins
Current used-market EV pricing is materially below comparable used gas F-150 pricing in this model
NY commercial electricity at a municipal facility still undercuts gasoline on a per-mile basis
Municipal charging-site incentives can improve the EV case further, but were kept out of the vehicle TCO table
Notes: [Sources] - Ford 2025 F-150 pricing/specs: https://www.ford.com/trucks/f150/2025/ - Ford 2025 F-150 Lightning pricing/specs and maintenance note: https://www.ford.com/trucks/f150-lightning/ - FuelEconomy.gov 2025 F-150 Pickup 4WD: https://www.fueleconomy.gov/feg/noframes/49143.shtml - FuelEconomy.gov 2025 F-150 Lightning 4WD SR: https://www.fueleconomy.gov/feg/PowerSearch.do?action=noform&baseModel=F-150+Lightning&make=Ford&pageno=1&srchtyp=ymm&year1=2025&year2=2025 - EIA Electric Power Monthly Table 5.6.A. (NY commercial electricity): https://www.eia.gov/electricity/monthly/epm_table_grapher.php?t=epmt_5_6_a - AAA state gas prices: https://gasprices.aaa.com/state-gas-price-averages/ - AAA Your Driving Costs 2025: https://newsroom.aaa.com/wp-content/uploads/2025/09/AAA-Brochure-Your-Driving-Cost-9.2025.pdf - J.D. Power used-vehicle pages: https://www.jdpower.com/cars/2023/ford/f-150/crew-cab-xlt-4wd and https://www.jdpower.com/cars/2023/ford/f-150-lightning-pickup/crew-cab-xlt-awd

## Slide 4
Key modeling assumptions
Assumptions were selected to fit a New York municipal fleet context with charging at a village facility
Purchase-price anchors
New F-150 XLT: $45,695 MSRP
New F-150 Lightning XLT: $63,345 MSRP
Included EV rebate: $500 NYSERDA Drive Clean on a new eligible Lightning
Used purchase anchors: 2023 XLT market comps (gas $44,650; Lightning $37,063)
Operating assumptions
Gas truck efficiency: 20 MPG
Lightning efficiency: 49 kWh / 100 miles
NY gasoline price: $4.10 / gallon
NY commercial electricity price: $0.2228 / kWh
Other cost inputs
Insurance and maintenance based on AAA pickup-truck benchmarks
EV maintenance set below gas-truck maintenance using Ford / AAA direction
Resale values modeled from current used-market anchors and forward depreciation assumptions
Interpretation note
The biggest unknown is future resale value, especially for EV pickups. The relative recommendation is strongest because the used Lightning starts from a materially lower purchase price in the current market.
Notes: [Sources] - Ford 2025 F-150 pricing/specs: https://www.ford.com/trucks/f150/2025/ - Ford 2025 F-150 Lightning pricing/specs and maintenance note: https://www.ford.com/trucks/f150-lightning/ - FuelEconomy.gov 2025 F-150 Pickup 4WD (20 MPG): https://www.fueleconomy.gov/feg/noframes/49143.shtml - FuelEconomy.gov 2025 F-150 Lightning 4WD SR (49 kWh/100 mi): https://www.fueleconomy.gov/feg/PowerSearch.do?action=noform&baseModel=F-150+Lightning&make=Ford&pageno=1&srchtyp=ymm&year1=2025&year2=2025 - EIA Electric Power Monthly Table 5.6.A. (NY commercial electricity): https://www.eia.gov/electricity/monthly/epm_table_grapher.php?t=epmt_5_6_a - AAA state gas prices: https://gasprices.aaa.com/state-gas-price-averages/ - AAA Your Driving Costs 2025: https://newsroom.aaa.com/wp-content/uploads/2025/09/AAA-Brochure-Your-Driving-Cost-9.2025.pdf - J.D. Power used-vehicle pages: https://www.jdpower.com/cars/2023/ford/f-150/crew-cab-xlt-4wd and https://www.jdpower.com/cars/2023/ford/f-150-lightning-pickup/crew-cab-xlt-awd

## Slide 5
Municipal and New York incentive lens
Vehicle-purchase incentives are modest; charging-site incentives could still be meaningful
Included in the TCO model
NYSERDA Drive Clean Rebate is open to residents, businesses, and government entities
For EVs with MSRP above $42,000, the rebate is $500
Applied only to the new-Lightning scenario
Kept out of the vehicle table
O&R POWERREADY incentives for site make-ready costs
Charge Ready NY 2.0 rebate per Level 2 port
Federal Section 30C elective-pay credit for eligible governmental charging projects
Not assumed in this deck
DEC municipal vehicle / infrastructure grant economics were not baked into the truck TCO
Current published DEC infrastructure window referenced publicly ran through February 27, 2026
DEC infrastructure support and NYSERDA Charge Ready cannot be used together for the same installation
Bottom line: the EV recommendation in this deck does not depend on assuming a large vehicle rebate.
Notes: [Sources] - NYSERDA Drive Clean Rebate: https://www.nyserda.ny.gov/All-Programs/Drive-Clean-Rebate-For-Electric-Cars-Program - O&R POWERREADY: https://www.oru.com/en/our-energy-future/electric-vehicles/new-york/commercial-ev-drivers/power-ready-program - IRS Section 30C credit for tax-exempt entities: https://www.irs.gov/credits-deductions/alternative-fuel-vehicle-refueling-property-credit-for-tax-exempt-entities - DEC municipal ZEV infrastructure / rebate notice: https://dec.ny.gov/news/press-releases/2025/10/dec-announces-funding-now-available-for-electric-vehicles-and-charging-stations-for-municipalities

## Slide 6
Total cost of ownership at 12,000 miles per year
Used F-150 Lightning is lowest-cost in all three holding periods
Chart: 
| 3 years | 5 years | 7 years
New F-150 gas | 26.6 | 44.5 | 61.5
New F-150 Lightning | 43 | 60.4 | 75.2
Used F-150 gas | 28.5 | 45.5 | 61.7
Used F-150 Lightning | 25.7 | 38.9 | 51.8
Exact modeled TCO
Option
3 years
5 years
7 years
New F-150 gas
$26.6k
$44.5k
$61.5k
New F-150 Lightning
$43.0k
$60.4k
$75.2k
Used F-150 gas
$28.5k
$45.5k
$61.7k
Used F-150 Lightning
$25.7k
$38.9k
$51.8k
Key takeaway
At 3 years, used Lightning is ~$0.9k cheaper than the next-best option
At 5 years, used Lightning is ~$5.6k below a new gas F-150
At 7 years, used Lightning is ~$9.7k below the next-best option
Notes: [Sources] - Ford 2025 F-150 pricing/specs: https://www.ford.com/trucks/f150/2025/ - Ford 2025 F-150 Lightning pricing/specs and maintenance note: https://www.ford.com/trucks/f150-lightning/ - FuelEconomy.gov 2025 F-150 Pickup 4WD (20 MPG): https://www.fueleconomy.gov/feg/noframes/49143.shtml - FuelEconomy.gov 2025 F-150 Lightning 4WD SR (49 kWh/100 mi): https://www.fueleconomy.gov/feg/PowerSearch.do?action=noform&baseModel=F-150+Lightning&make=Ford&pageno=1&srchtyp=ymm&year1=2025&year2=2025 - EIA Electric Power Monthly Table 5.6.A. (NY commercial electricity): https://www.eia.gov/electricity/monthly/epm_table_grapher.php?t=epmt_5_6_a - AAA state gas prices: https://gasprices.aaa.com/state-gas-price-averages/ - AAA Your Driving Costs 2025: https://newsroom.aaa.com/wp-content/uploads/2025/09/AAA-Brochure-Your-Driving-Cost-9.2025.pdf - J.D. Power used-vehicle pages: https://www.jdpower.com/cars/2023/ford/f-150/crew-cab-xlt-4wd and https://www.jdpower.com/cars/2023/ford/f-150-lightning-pickup/crew-cab-xlt-awd

## Slide 7
Total cost of ownership at 15,000 miles per year
This is the most balanced “typical fleet” case
Chart: 
| 3 years | 5 years | 7 years
New F-150 gas | 29.5 | 49.3 | 68.2
New F-150 Lightning | 44.6 | 63 | 78.9
Used F-150 gas | 31.6 | 50.7 | 68.9
Used F-150 Lightning | 27.4 | 41.8 | 55.8
Exact modeled TCO
Option
3 years
5 years
7 years
New F-150 gas
$29.5k
$49.3k
$68.2k
New F-150 Lightning
$44.6k
$63.0k
$78.9k
Used F-150 gas
$31.6k
$50.7k
$68.9k
Used F-150 Lightning
$27.4k
$41.8k
$55.8k
Key takeaway
At 5 years, used Lightning is ~$7.5k cheaper than a new gas F-150
At 7 years, the gap widens to ~$12.4k vs. the next-best option
New Lightning remains the highest-cost path despite lower operating cost
Notes: [Sources] - Ford 2025 F-150 pricing/specs: https://www.ford.com/trucks/f150/2025/ - Ford 2025 F-150 Lightning pricing/specs and maintenance note: https://www.ford.com/trucks/f150-lightning/ - FuelEconomy.gov 2025 F-150 Pickup 4WD (20 MPG): https://www.fueleconomy.gov/feg/noframes/49143.shtml - FuelEconomy.gov 2025 F-150 Lightning 4WD SR (49 kWh/100 mi): https://www.fueleconomy.gov/feg/PowerSearch.do?action=noform&baseModel=F-150+Lightning&make=Ford&pageno=1&srchtyp=ymm&year1=2025&year2=2025 - EIA Electric Power Monthly Table 5.6.A. (NY commercial electricity): https://www.eia.gov/electricity/monthly/epm_table_grapher.php?t=epmt_5_6_a - AAA state gas prices: https://gasprices.aaa.com/state-gas-price-averages/ - AAA Your Driving Costs 2025: https://newsroom.aaa.com/wp-content/uploads/2025/09/AAA-Brochure-Your-Driving-Cost-9.2025.pdf - J.D. Power used-vehicle pages: https://www.jdpower.com/cars/2023/ford/f-150/crew-cab-xlt-4wd and https://www.jdpower.com/cars/2023/ford/f-150-lightning-pickup/crew-cab-xlt-awd

## Slide 8
Total cost of ownership at 20,000 miles per year
The EV operating-cost benefit becomes more visible as mileage rises
Chart: 
| 3 years | 5 years | 7 years
New F-150 gas | 34.3 | 57.3 | 79.3
New F-150 Lightning | 47.3 | 67.4 | 85.1
Used F-150 gas | 36.7 | 59.2 | 80.8
Used F-150 Lightning | 30.2 | 46.6 | 62.5
Exact modeled TCO
Option
3 years
5 years
7 years
New F-150 gas
$34.3k
$57.3k
$79.3k
New F-150 Lightning
$47.3k
$67.4k
$85.1k
Used F-150 gas
$36.7k
$59.2k
$80.8k
Used F-150 Lightning
$30.2k
$46.6k
$62.5k
Key takeaway
At 5 years, used Lightning is ~$10.7k cheaper than a new gas F-150
At 7 years, used Lightning is ~$16.8k cheaper than the next-best option
Higher annual miles strengthen the recommendation for the used Lightning
Notes: [Sources] - Ford 2025 F-150 pricing/specs: https://www.ford.com/trucks/f150/2025/ - Ford 2025 F-150 Lightning pricing/specs and maintenance note: https://www.ford.com/trucks/f150-lightning/ - FuelEconomy.gov 2025 F-150 Pickup 4WD (20 MPG): https://www.fueleconomy.gov/feg/noframes/49143.shtml - FuelEconomy.gov 2025 F-150 Lightning 4WD SR (49 kWh/100 mi): https://www.fueleconomy.gov/feg/PowerSearch.do?action=noform&baseModel=F-150+Lightning&make=Ford&pageno=1&srchtyp=ymm&year1=2025&year2=2025 - EIA Electric Power Monthly Table 5.6.A. (NY commercial electricity): https://www.eia.gov/electricity/monthly/epm_table_grapher.php?t=epmt_5_6_a - AAA state gas prices: https://gasprices.aaa.com/state-gas-price-averages/ - AAA Your Driving Costs 2025: https://newsroom.aaa.com/wp-content/uploads/2025/09/AAA-Brochure-Your-Driving-Cost-9.2025.pdf - J.D. Power used-vehicle pages: https://www.jdpower.com/cars/2023/ford/f-150/crew-cab-xlt-4wd and https://www.jdpower.com/cars/2023/ford/f-150-lightning-pickup/crew-cab-xlt-awd

## Slide 9
Sensitivity summary
Across the tested range, the same answer holds: the used F-150 Lightning is the lowest-cost option
Cheapest option in each case
3 years
5 years
7 years
12k
mi/yr
Used Lightning
$25.7k
beats next-best by $0.9k
Used Lightning
$38.9k
beats next-best by $5.6k
Used Lightning
$51.8k
beats next-best by $9.7k
15k
mi/yr
Used Lightning
$27.4k
beats next-best by $2.1k
Used Lightning
$41.8k
beats next-best by $7.5k
Used Lightning
$55.8k
beats next-best by $12.4k
20k
mi/yr
Used Lightning
$30.2k
beats next-best by $4.1k
Used Lightning
$46.6k
beats next-best by $10.7k
Used Lightning
$62.5k
beats next-best by $16.8k
Implication for the Board
Recommendation is not dependent on a single mileage assumption
The cost advantage grows as annual mileage rises
The case for a new Lightning remains weak on pure dollars
The main non-financial decision factors are towing duty cycle, charging logistics, and used-vehicle condition
Notes: [Sources] - Ford 2025 F-150 pricing/specs: https://www.ford.com/trucks/f150/2025/ - Ford 2025 F-150 Lightning pricing/specs and maintenance note: https://www.ford.com/trucks/f150-lightning/ - FuelEconomy.gov 2025 F-150 Pickup 4WD (20 MPG): https://www.fueleconomy.gov/feg/noframes/49143.shtml - FuelEconomy.gov 2025 F-150 Lightning 4WD SR (49 kWh/100 mi): https://www.fueleconomy.gov/feg/PowerSearch.do?action=noform&baseModel=F-150+Lightning&make=Ford&pageno=1&srchtyp=ymm&year1=2025&year2=2025 - EIA Electric Power Monthly Table 5.6.A. (NY commercial electricity): https://www.eia.gov/electricity/monthly/epm_table_grapher.php?t=epmt_5_6_a - AAA state gas prices: https://gasprices.aaa.com/state-gas-price-averages/ - AAA Your Driving Costs 2025: https://newsroom.aaa.com/wp-content/uploads/2025/09/AAA-Brochure-Your-Driving-Cost-9.2025.pdf - J.D. Power used-vehicle pages: https://www.jdpower.com/cars/2023/ford/f-150/crew-cab-xlt-4wd and https://www.jdpower.com/cars/2023/ford/f-150-lightning-pickup/crew-cab-xlt-awd

## Slide 10
Recommendation and decision points
Recommended acquisition path: buy a used Ford F-150 Lightning
Recommendation
Authorize procurement of a
used F-150 Lightning
Lowest modeled TCO in every mileage and holding-period case tested
Best fit for a village-owned charging location in O&R territory
Recommendation does not require assuming a large vehicle rebate
Board questions to validate before award
Topic
What to confirm
Vehicle condition
Mileage, battery health / diagnostics, warranty status, accident history
Operational fit
Expected towing duty, winter range expectations, payload use
Charging plan
Number of plugs needed, site readiness, O&R / NYSERDA timing
Procurement price
Final dealer quote, delivery timing, any incremental equipment needs
If the Board wants a second-stage diligence step, the most useful next analysis is charger-site economics allocated across 1, 2, and 5 fleet vehicles.
This deck is designed as a decision-support tool rather than a formal procurement specification.
Notes: [Sources] - Ford 2025 F-150 pricing/specs: https://www.ford.com/trucks/f150/2025/ - Ford 2025 F-150 Lightning pricing/specs and maintenance note: https://www.ford.com/trucks/f150-lightning/ - FuelEconomy.gov 2025 F-150 Pickup 4WD (20 MPG): https://www.fueleconomy.gov/feg/noframes/49143.shtml - FuelEconomy.gov 2025 F-150 Lightning 4WD SR (49 kWh/100 mi): https://www.fueleconomy.gov/feg/PowerSearch.do?action=noform&baseModel=F-150+Lightning&make=Ford&pageno=1&srchtyp=ymm&year1=2025&year2=2025 - EIA Electric Power Monthly Table 5.6.A. (NY commercial electricity): https://www.eia.gov/electricity/monthly/epm_table_grapher.php?t=epmt_5_6_a - AAA state gas prices: https://gasprices.aaa.com/state-gas-price-averages/ - AAA Your Driving Costs 2025: https://newsroom.aaa.com/wp-content/uploads/2025/09/AAA-Brochure-Your-Driving-Cost-9.2025.pdf - NYSERDA Drive Clean Rebate: https://www.nyserda.ny.gov/All-Programs/Drive-Clean-Rebate-For-Electric-Cars-Program - O&R POWERREADY: https://www.oru.com/en/our-energy-future/electric-vehicles/new-york/commercial-ev-drivers/power-ready-program - IRS Section 30C credit for tax-exempt entities: https://www.irs.gov/credits-deductions/alternative-fuel-vehicle-refueling-property-credit-for-tax-exempt-entities - DEC municipal ZEV infrastructure / rebate notice: https://dec.ny.gov/news/press-releases/2025/10/dec-announces-funding-now-available-for-electric-vehicles-and-charging-stations-for-municipalities - J.D. Power used-vehicle pages: https://www.jdpower.com/cars/2023/ford/f-150/crew-cab-xlt-4wd and https://www.jdpower.com/cars/2023/ford/f-150-lightning-pickup/crew-cab-xlt-awd